## Slide 1: AI-based Real-time Energy optimization Model at Ironmaking
A Vision to Execute Better.
Everyday.
Peddinti Bhuvaneswara Rao
Keshav Baheti
Mentor: Mr. Naveen Singh
Buddy: Mr. Mohanraj Nagarajan

## Slide 2
Project Overview
Ironmaking process adopts relatively complete process technology and equipment, which provides a good research and development foundation and supporting environment for the application of blast furnace big data technology and the improvement of the level of ironmaking intelligence.
During the long-term operation of the blast furnace, a large amount of smelting process data will be accumulated, giving full play to the value of big data, and deep mining of the inherent laws contained in big data through artificial intelligence technology.
The blast furnace process is a "black box" operation, and the smelting process is unpredictable.
Effectively forecasting and guiding production, and finally achieving refined and intelligent ironmaking, is of great significance to the steel industry.

## Slide 3
Project Goals
Cleaning and processing of Blast Furnace data to identify the interrelationships between input and output parameters.
Energy balance in blast furnace by finding input and output energies
Optimization techniques to minimize input energy
Developing of constraints on the input parameters using the interrelation of input and output parameters from historical data

## Slide 4: Agenda
Overview of The Blast Furnace
Calculation of Output energy
Input and output energy composition at different conditions
Optimization techniques to get optimal input parameters
Calculation of Input Energy

## Slide 5: Agenda
Overview of The Blast Furnace
Calculation of Output energy
Input and output energy composition at different conditions
Optimization techniques to get optimal input parameters
Calculation of Input Energy

## Slide 6
1
Energy Consumption in steel industry, Gcal/tcs
Chart: 
| Ukraine | China | India | Brazil | Japan | Russia | France | Vietnam | South Korea | Germany | Canada | EU-27 | USA | Mexico | Turkey | Italy
 | 6.2141 | 4.8996 | 4.7801 | 4.7323 | 4.6606 | 4.5411 | 4.4216 | 4.3021 | 4.0631 | 3.8719 | 3.8241 | 3.609 | 3.1071 | 2.9876 | 2.6291 | 2.3901
2
Energy Consumption in JSW VJNR, Gcal/tcs
Energy Consumption in EU, USA countries are low – Due to more scrap & low grid emission factor
Corex, Blast Furnace & Mill Zone are high energy consumption units
ISP Energy Intensity | Global Steel Industry

## Slide 7
Chart: 
| World | Mexico | Ukraine | Vietnam | Taiwan | Italy | Iran | Brazil | Germany | Turkey | South Korea | Russia | USA | Japan | India | China
 | 70.8 | 15.9 | 76 | 35.6 | 60.5 | 16 | 9.7 | 75.2 | 69.8 | 28.4 | 68.2 | 59 | 30.8 | 74.7 | 44.8 | 89.4
 | 29.2 | 84.1 | 24 | 64.4 | 39.5 | 84 | 90.3 | 24.8 | 30.2 | 71.6 | 31.8 | 41 | 69.2 | 25.3 | 55.2 | 10.6
Oxygen Route
Electric Route
Presently 70% of production through oxygen route & 30 % from electric route
If China is not considered, then ratio will be 52 % :48 %
2
70% Steel Production Route CO2 Emission break up, TCO2/TCS
~50 % of CO2 emission is from Blast Furnace
~15% of CO2 emission are from Sinter Plant
1
Global Steel Production Route, %
Steel Route & CO2 Emission | Global Steel Industry

## Slide 8
CO2 Emission Contributions – Shop Level
Steel Zone contributed to ~18% of total emissions
Chart: 
 | 2.45
CO2 emissions (kg CO2/tcs) FY24 Actual
CO2 Emissions – Plant level
2.63 tons/tcs CO2 emissions in FY24
Chart: 
| OBP | LP Mills | COP | CRM | DRI | Others | HSM | Pellet | LCP | Corex | SMS | Sinter | BF
kg CO2/tcs | 21 | 44 | 62 | 72 | 78 | 98 | 116 | 129 | 151 | 191 | 238 | 297 | 1134
kg CO2/TCS
#Others: CPP, Boilers, Building lighting, etc.
CO2 | Emissions

## Slide 9: Overview of Blast Furnace
Long Term
INPUTS
OUTPUTS
The outputs of a blast furnace are molten iron (called pig iron) and slag.
A blast furnace is a type of furnace used in metallurgy to produce iron from iron ore using a combination of coke as fuel and limestone as a flux.
It operates by continuously
feeding iron ore, coke, and fluxes
into the top, where a blast of hot air
or oxygen is blown through tuyeres (nozzles) at the base. This process produces molten iron and slag (a byproduct), which are tapped from
the bottom of the furnace.

## Slide 10
Overview of Blast Furnace

## Slide 11
Time lag and Steady state operation of blast furnace
There is a time lag of about 4-5 hours, from the time when the raw material is added and the time when the output material is tapped due to the pressure applied by hot blast gas. This leads to decrease in speed of descent of material dropped from top of the Blast Furnace
The Principal components are Burden descent rate, Top gas Temperature, Gas Utilization, Differential Pressures and gas Permeability resistance for predicting the Hot Metal Temperature. Channeling is a non-homogenous condition of the Burden distribution where ascending gases tries to preferentially flow, resulting in changes in the Gas flow pattern in top gas and subsequently affects the Burden movement down the stock line.
During residence of hot metal inside the blast furnace, the hot metal comes in contact with dead man zone and hearth refractory, wherein the gradual thermal loss takes place. So, the longer it remains in the blast furnace the cooler it’s temperature gets.

## Slide 12: Current method to find the amount of Coke and Coal
The present method for the amount of coke and coal used in one batch of Blast furnace operation depends upon the Hot Metal Temperature.
There is a fixed minimum value of Coke to be added per ton hot metal, then they add or remove the amount of coke based upon the hot metal temperature.
The problem with this method is:
There is delay in the time at which load is added and the time at which hot metal is tapped about a delay of 4-5 hours.
There is no Hot Metal prediction model for Blast Furnace-4 also the reading of the hot metal temperature is not taken hourly
The Temperature of Hot Metal varies from Tap hole to Tap hole due to the formation of Deadman inside the Blast furnace.
The Hot Metal Temperature depends on many other factors: Burden descent rate, Top gas Temperature, Gas Utilization(ETACO), Differential Pressures and Gas Permeability Resistance.
It also depends on Channeling, Channeling is condition of the Burden distribution where ascending gases tries to preferentially flow, resulting in changes in the Gas flow pattern in top gas and subsequently affects the Burden movement.

## Slide 13: Blast Furnace – 4 | JSW Vijayanagar
Parameter | Value
Production | 9830 t/day
Productivity (w/v) | 2.5 t/m³/day
Fuel Rate | 2.5 t/m³/day
Coke Rate | 520 Kg/THM
PCI Rate | 380 Kg/THM
Slag Rate | 160 Kg/THM
Sinter / Pellet / Lump Ore (%) | 80/10/10
Hot Blast Pressure | 4 bar
High Top Pressure | 2.5 bar
Hot Blast Temp | 1250°C
Cold Blast Volume | 5800 Nm³/min
O2 enrichment | 5-7%
Gas make | 525000 Nm³/hr
Area | Value | Unit
Diameter Throat | 9.6 | m
Belly | 15.16 | m
Hearth | 13.2 | m
Heights Throat | 1.57 | m
Stack | 17.6 | m
Belly | 3 | m
Bosh | 3.5 | m
Tuyere to Bosh | 0.6 | m
Taphole to Tuyere | 4.2 | m
Bottom to Taphole | 3.1 | m
Tap hole level | 11.06 | m
Tuyeres level | 15 | m
Furnace Top | 47.14 | m
Working | 26.3 | m
Total | 33.6 | m
Volumes Working | 3445 | m³
Inner | 4020 | m³
Production/hearth area | 57 | t/day/m2 hearth
Stack | 81.02 | Degrees
Bosh | 74.36 | Degrees
Design Data
Operating Parameters

## Slide 14: Full forms and Definitions
Here percentages are taken from Blast Furnace’s top gas Composition
TRT Power Generation- This Power is generated due to kinetic energy of top gas by turning a turbine
All the energies are calculated for per tonne of hot metal (thm).
Abbreviation | Definition
N2 | Nitrogen
O2 | Oxygen
CO | Carbon Monoxide
CO2 | Carbon Dioxide
CDI | Coal Dust Injection
PCI | Pulverized Coal Injection
Kcal | Kilo Calorie
H2 | Hydrogen
Fe | Iron
Mn | Manganese
BF Gas | Blast furnace Gas
TRT | Top gas Recovery Turbine
KPI | Key Performance Index
Thm | Tonne Hot Metal
Nm3 | Normal Meter Cube
ETA CO | Carbon Utilization Efficiency

## Slide 15: Agenda
Overview of The Blast Furnace
Calculation of Output energy
Input and output energy composition at different conditions
Optimization techniques to get optimal input parameters
Calculation of Input Energy

## Slide 16
Input energy calculations
1.Energy from coke:
)
2.Energy from CDI (Coal Dust Injection):
3. Energy from Hot Blast (Mainly N₂ and O₂):
4. Energy from Steam:
5.Kinetic Energy of Hot Blast:
Calorific Value of Pure carbon = 7800 Kcal/kg
Late heat of Vaporization = 540 Cal/kg
Specific heat of water = 1 Kcal/kg
Specific Heat of O2 = 0.22 Kcal/kg.
Specific Heat of N2 = 0.25 Kcal/kg.
Fixed Carbon is the amount of pure carbon in Coke/Coal
The Base Temperature is taken at 25 Degree Celsius and all energies are calculated per Ton of Hot Metal

## Slide 17: Agenda
Overview of The Blast Furnace
Calculation of Output energy
Input and output energy composition at different conditions
Optimization techniques to get optimal input parameters
Calculation of Input Energy

## Slide 18
Volume from the Flow Sensor
Volume from the Gas Sensor data using the N2 Conservation in both Input and Output
Blast Furnace Gas Calculation
Chart: Volume Comparison Graph

## Slide 19
Energy Lost due to unburnt carbon (CO) in the BF gas
Thermal energy of BF gas
Thermal energy in Hot Metal
Thermal Energy in slag
Energy lost due to unburnt carbon dissolved in Hot metal
Output energy calculations

## Slide 20
Energy lost in Dust in the from of carbon
Energy lost in Metalloid Reactions(Fe2O3 to Fe, Mn2O3 to Mn and so..on.. n Metals etc)
Energy generated from TRT-power generator
(Other Heat Losses)
9. Energy lost in convection due to flow of steam around Blast Furnace lining
10. Kinetic energy of the Hot metal flowing into the Torpedoes
Output Energy Calculations

## Slide 21: Agenda
Overview of The Blast Furnace
Calculation of Output energy
Input and output energy composition at different conditions
Optimization techniques to get optimal input parameters
Calculation of Input Energy

## Slide 22
From the Historical data of blast furnace input and output energies were calculated and their composition at different instances were recorded
Input energy composition
At Higher Input Energy Average energy: 3858442.951 Kcal/thm
At Lower Input Energy Average energy: 3609876.806 Kcal/thm

## Slide 23
Output energy composition
At Higher Input Energy Average Energy: 3858442.951 Kcal/thm
At Lower Input Energy Average energy: 3609876.806 Kcal/thm

## Slide 24
Water-cooled blast furnace cooling element - called a stave. These staves are attached to the inside of the blast furnace walls. Cooling staves can made from copper or cast iron. Their job is to maintain the structural integrity of the furnace by cooling the walls. Cool water is pumped into, around, and out of a hollow flow pattern or pipe inside the stave - removing heat from the furnace wall. In service, the grooved interior face (left) is packed with refractory bricks. Many other water cooling shapes are used as needed
Unaccounted Heat losses
*Source : blast-furnace-ironmaking-analysis-control-and-optimization

## Slide 25
Chart: 
Input and Output Energies of Blast Furnace
The calculated output energy accounts for 70% of input energy and remaining 30% of input energy is unaccounted energy loss

## Slide 26: Agenda
Overview of The Blast Furnace
Calculation of Output energy
Input and output energy composition at different conditions
Optimization techniques to get optimal input parameters
Calculation of Input Energy

## Slide 27
Model1: Data training and Prediction Model
Data Collection and Cleaning
Splitting Data into training and testing sets
Training of gradientBoostingRegressor - model with data
Generation of objective function for input energy
Minimizing objective function using - trained data
Output

## Slide 28
Code for Prediction Model(Model 1)
Minimized Input Energy: 3034787.99 Kcal/thm
Optimal Input Parameters (Original Scale):
Hot Metal (Batches)Tons: 9862.38
Total Coke: 325.90 kg/thm
CDI : 199.68 kg/thm
Steam addition : 14.72 kg/thm
Hot Blast Temp: 1146.65 °C
O2 vol : 275.37 Nm3/thm
N2 vol : 639.32 Nm3/thm
Results Of this Model 1

## Slide 29
Method2: Linear Optimization model
Minimizing objective function - using Linear Optimisation
Preparation of Objective function for input energy
Obtaining Constraints on Output Parameters
Selecting KPI’s in Output Parameters
Obtaining Constraints on Input …..parameters using output constraints
Output

## Slide 30
Important KPIs for the Blast Furnace
Hot Metal Temperature
Hot Metal Carbon
Hot Metal Production
CO Emission per thm
Total Input Energy
ETA CO
Input and Output Parameter Selection
The Input Parameters are the Parameters
in the Input Energy Equation
The volume of O2 added from Hot Blast
The volume of N2 added from Hot Blast
The amount of Coal added
The amount of Coke added
The Hot Blast Temperature

## Slide 31
Constraints on the Output Parameter
The Constraints on the Output Parameter are based
on the Past Data trends as well as the Optimal or
Threshold value of the parameter
Hot Metal Temperature (1450 – 1510) °C
Hot Metal Carbon (40-45.5 Kg/thm)
Hot Metal Production (> 9600 tons/day)
Input Energy (<3.75 Gcal/thm)
CO emission in BF-gas (300 – 350 vol/thm)
Eta CO ( CO/(CO+CO2)) (0.5-0.55)

## Slide 32
Correlation heat map between I/p and O/p parameters

## Slide 33
Correlation heat map for Hot metal carbon and Hot Metal Temperature with other parameters
From the above correlation matrix, it is concluded that Hot Metal Carbon and Hot Metal Temperature have no relation with any parameter, so we used the charts of past data to find the constraints on input parameters with respect to these output parameters

## Slide 34
Methodology for finding the constraints
Output parameter constraints were selected based on the optimal value for the operation of blast furnace and analyzing furnace’s historical data
For the Input Parameters having no correlation with the Output Parameter, charts were plotted between input and output parameters(which are mainly KPI’s) and charts were visually analyzed for Input constraints. At last ranges on the output parameters were obtained by studying charts within constraints of output parameters.
Intersection of each Input parameters constraints which were obtained after inspecting it through all output parameters(which are KPI’s) were taken into consideration for using them in Optimization technique.
Coke<= -0.04375*HMP+771
Coke>=-0.025HP+558
CDI<=(0.025HMP-36)
CDI>=(0.035HMP-158)
Chart: Coke (kg) v/s Hot Metal Production tons/day
Chart: CDI (kg) v/s Hot Metal Production tons/day

## Slide 35
Constraints on Coke
Chart: Coke (kg) v/s Hot metal temp(°C)
Chart: Coke (kg) v/s input energy(in Kcal)
Chart: Coke (kg) v/s CO (Nm3)
Chart: Coke (kg) v/s C in Hot Metal(kg)
 | Hot Metal Production | CO Volume | ETA CO | Hot metal Carbon | Input Energy | Hot metal Temperature
Coke | 300-350 Coke<= -0.04375*HMP+771 coke>=-0.025HP+558 | 300-350 | 304-350 Coke<=2307*ETACO-829 | 305-350 | 300-335 | No Relation
Chart: Coke (kg) v/s Hot Metal Production tons/day
Chart: Coke (kg) v/s ETA CO

## Slide 36
Constraints on CDI
 | Hot Metal Production | CO Volume | ETA CO | Hot metal Carbon | Input Energy | Hot metal Temperature
CDI | 180-220 CDI<=(0.025HMP-36) CDI>=(0.035HMP-158) | 185-215 | 180-216 | 160-220 | 190-215 | No Relation
Chart: Coke (kg) v/s Hot metal temp(°C)
Chart: CDI (kg) v/s input energy(Kcal)
Chart: CDI (kg) v/s CO (Nm3)
Chart: CDI (kg) v/s C in Hot Metal(kg)
Chart: CDI (kg) V/S ETA CO
Chart: CDI (kg) v/s Hot Metal Production tons/day

## Slide 37
Constraints on Oxygen(O2)
 | Hot Metal Production | CO Volume | ETA CO | Hot metal Carbon | Input Energy | Hot metal Temperature
O2 | 265-290 O2<=-0.026*HMP+542 | 263-287 | 264-290 O2<=785.2*ETACO-116.45 | 260-300 | 265-285 | 265-295
Chart: O2 (Nm3) vs Hot Metal Production (tons/day)
Chart: O2 (Nm3) vs Hot Metal Temperature(°C)
Chart: O2 (Nm3) vs C in Hot Metal(Kg)
Chart: O2 (Nm3) v/s Input Energy(Kcal)
Chart: O2 (Nm3) v/s CO (Nm3)
Chart: O2 (Nm3) v/s ETA CO

## Slide 38
Constraints on Nitrogen (N2)
 | Hot Metal Production | CO Volume | ETA CO | Hot metal Carbon | Input Energy | Hot metal Temperature
N2 | 620-665 N2<=-0.063*HMP+1267 N2>=-0.0465*HMP+1089 | No Relation | 618-670 N2<=3506.9*ETACO-1120.3 | 620-690 | 615-665 | No Relation
Chart: N2 (Nm3) vs C in Hot Metal(kg)
Chart: N2 (Nm3) vs Hot Metal Temperature(°C)
Chart: N2 (Nm3) vs Hot Metal Production (tons/day)
Chart: N2(Nm3) v/s C in Input Energy(Kcal)
Chart: N2 (Nm3) v/s CO (Nm3)
Chart: N2 (Nm3) v/s ETA CO

## Slide 39
Constraints on Hot blast temperature
 | Hot Metal Production | CO Volume | ETA CO | Hot metal Carbon | Input Energy | Hot metal Temperature
Hot Blast Temperature | No Relation | No Relation | No Relation | No Relation | No Relation | No Relation
Chart: Hot Blast Temp. °C v/s Hot Metal Temperature (°C)
Chart: Hot Blast Temp. °C v/s C in Hot Metal(Kg)
Chart: Hot Blast Temp. °C v/s Input Energy(Kcal)
Chart: Hot Blast Temp. °C v/s CO(Nm3)
Chart: Hot Blast Temp. °C v/s Hot metal Production (tons/day)
Chart: Hot Blast Temp. °C v/s ETA CO

## Slide 40: *As there is no relation of Hot Blast Temperature with other parameters, a temperature of 1125 degree Celsius(most probable temperature ) is considered for optimal energy calculations
Final table of constraints for the input parameters
 | Hot Metal Production | CO Volume | ETA CO | Hot metal Carbon | Input Energy | Hot metal Temperature
Coke | 300-350 Coke<= -0.04375*HMP+771 coke>=-0.025HP+558 | 300-350 | 304-350 Coke<=2307*ETACO-829 | 305-350 | 300-335 | No Relation
CDI | 180-220 CDI<=(0.025HMP-36) CDI>=(0.035HMP-158) | 185-215 | 180-216 | 160-220 | 190-215 | No Relation
O2 | 265-290 O2<=-0.026*HMP+542 | 263-287 | 264-290 O2<=785.2*ETACO-116.45 | 260-300 | 265-285 | 265-295
N2 | 620-665 N2<=-0.063*HMP+1267 N2>=-0.0465*HMP+1089 | No Relation | 618-670 N2<=3506.9*ETACO-1120.3 | 620-690 | 615-665 | No Relation
Hot Blast Temperature | No Relation | No Relation | No Relation | No Relation | No Relation | No Relation

## Slide 41: Linear Programming
Using the input energy equation, we apply Linear Programming to the equation.
The primary goal of LP is to minimize the linear objective function, subject to a set of linear equality and inequality constraints.
Linear programming is a method to achieve the best outcome in a mathematical model whose requirements are represented by linear relationships
The components of the equation are the input energy components of which we have found the constraints for, now we apply Linear Programming in Python. Giving us the minimum value of the energy for particular set of values of the input parameters.

## Slide 42
Code of Linear Optimization Technique(Model 2)
Minimized Input Energy: 3562549.2 Kcal/thm
Optimal Input Parameters (Original Scale):
Hot Metal (tons): 10000
Total Coke: 308.00 kg/thm
CDI kg/thm: 192.00
Steam addition kg/thm: 5.00
Hot Blast Temp. °C: 1125.00
O2 weight(Kg)/thm: 378.00
N2 weight(Kg)/thm: 768.00
Results Of this Model 2

## Slide 43: *source: IndiaMart
Cost Analysis After Model Implementation
By Present Method
For financial year April’23 to March’24
There are 255 days where production is greater than 9600 tons/day.Only those days were considered for Cost calculation.
Total Hot metal production = 2516434 tons
Total amount of coke consumed = 82,00,96,640 kg
Total amount of coal consumed = 507749023 kg
Price of coke= Rs 12400/ton
Price of coal = Rs 4000/ton
Amount spent on coke =(820096640/1000)*12400
= Rs 10169198334
Amount spent on coal =(507749023/1000)*4000
= Rs 2030996092
Total amount spent =Rs. 12200194426
After Model Implementation
From present method for same amount of production i.e. 2516434 tons of hot metal
Amount spent on coke in Rupees after implementing the model =(2516434*308/1000*12400)
=Rs 9610765799
Amount spent on coke in Rupees after implementing the model =(2516434*192/1000*4000)
=Rs 1932621526
Total Amount Spent
=Rs 9610765799 + 1932621526
= 11543387325

## Slide 44
Amount spent on Coke and Coal using present method
1220 Cr.
Amount spent on Coke and Coal after implementing the model
1154.5 Cr
Amount Saved
65.5 Cr
Cost Analysis After Model Implementation
Money spent on the Coke and Coal Can be decreased by 5.36% after implementation of model
Amount of Carbon used is decreased by 69629 tonnes/annum